## Slide 1: Unit : 2 Basic Computer Organization and Design

## Slide 2
Instruction Code :
An instruction code is a group of bits that instruct the computer to perform a specific operation.
Operation Code :
The operation code of an instruction is a group of bits that define such operations as add, subtract, multiply, shift, and complement.
The number of bits required for the operation code of an instruction depends on the total number of operations available in the computer. The operation code must consist of at least n bits for a given 2n (or less) distinct operations.
Accumulator (AC)
Computers that have a single-processor register usually assign to it the name accumulator (AC) accumulator and label it AC.
The operation is performed with the memory operand and the content of AC.
Opcode | Operands

## Slide 3: Stored Program Organization :

## Slide 4: INSTRUCTION FORMAT
A computer instruction is often divided into two parts
  1. An opcode (Operation Code) that specifies the operation for that instruction
  2. An address that specifies the registers and/or locations in memory to use for that operation
In the Basic Computer, since the memory contains 4096 (= 212) words, we needs 12 bit to specify which memory address this instruction will use.
In the Basic Computer, bit 15 of the instruction specifies the addressing mode (0: direct addressing, 1: indirect addressing)
Since the memory words, and hence the instructions, are 16 bits long, that leaves 3 bits for the instruction’s opcode
Opcode
Address
Instruction Format
15
14
12
0
I
11
Addressing
mode

## Slide 5: ADDRESSING MODES :
The address field of an instruction can represent either
  Direct address: the address in memory of the data to use (the address of the operand), or
  Indirect address: the address in memory of the address in memory of the data to use
Effective Address (EA)
  The address, that can be directly used without modification to access an operand for a computation-type instruction, or as the target address for a branch-type instruction
0
ADD
457
22
Operand
457
1
ADD
300
35
1350
300
Operand
1350
+
AC
+
AC
Direct addressing
Indirect addressing

## Slide 6: Direct address :
2. Address is selected in memory and its Data placed on the bus to be loaded into the Data Register to be used for requested instructions
Occurs When the Operand Part Contains the Address of Needed Data.
1. Address part of IR is placed on the bus and loaded back into the AR

## Slide 7: Direct address

## Slide 8: Indirect address :
3. New Address is selected in memory and placed on the bus to be loaded into the DR to use later
2. Address is selected in memory and placed on the bus to be loaded Back into the AR
Occurs When the Operand Contains the Address of the Address of Needed Data.
1. Address part of IR is placed on the bus and loaded back into the AR

## Slide 9: Indirect address

## Slide 10: Effective address:
• Effective address: Address where an operand is physically located
Effective address: 457 Effective address: 1350

## Slide 11
Direct and Indirect addressing example
  Addressing Mode
Notes: 11

## Slide 12: Registers of basic computer :
 It is necessary to provide a register in the control unit for storing the instruction code after it is read from memory.
 The computer needs processor registers for manipulating data and a register for holding a memory address.
 These requirements dictate the register configuration shown in Figure
Figure : Basic Computer Register and Memory

## Slide 13
 The data register (DR) holds the operand read from memory.
 The accumulator (AC) register is a general purpose processing register.
The instruction read from memory is placed in the instruction register (IR).
 The temporary register (TR) is used for holding temporary data during the processing.
 The memory address register (AR) has 12 bits.
The program counter (PC) also has 12 bits and it holds the address of the next instruction to be read from memory after the current instruction is executed.
Instruction words are read and executed in sequence unless a branch instruction is encountered. A branch instruction calls for a transfer to a nonconsecutive instruction in the program.
 Two registers are used for input and output. The input register (INPR) receives an 8-bit character from an input device. The output register (OUTR) holds an 8-bit character for an output device.

## Slide 15: Common Bus System for basic computer register :
 The basic computer has eight registers, a memory unit and a control unit.
Paths must be provided to transfer information from one register to another and between memory and register.
The number of wires will be excessive if connections are between the outputs of each register and the inputs of the other registers. An efficient scheme for transferring information in a system with many register is to use a common bus.
 The connection of the registers and memory of the basic computer to a common bus system is shown in figure.

## Slide 17
 The outputs of seven registers and memory are connected to the common bus. The specific output that is selected for the bus lines at any given time is determined from the binary value of the selection variables S2, S1, and S0.
The number along each output shows the decimal equivalent of the required binary selection.
 The particular register whose LD (load) input is enabled receives the data from the bus during the next clock pulse transition. The memory receives the contents of the bus when its write input is activated. The memory places its 16-bit output onto the bus when the read input is activated and S2 S1 S0 = 1 1 1.
 Four registers, DR, AC, IR, and TR have 16 bits each.
Two registers, AR and PC, have 12 bits each since they hold a memory address.
When the contents of AR or PC are applied to the 16-bit common bus, the four most significant bits are set to 0’s. When AR and PC receive information from the bus, only the 12 least significant bits are transferred into the register.
 The input register INPR and the output register OUTR have 8 bits each and communicate with the eight least significant bits in the bus.

## Slide 18
 INPR is connected to provide information to the bus but OUTR can only receive information from the bus.
Five registers have three control inputs: LD (load), INR (increment), and CLR (clear). Two registers have only a LD input.
AR must always be used to specify a memory address; therefore memory address is connected to AR.
 The 16 inputs of AC come from an adder and logic circuit. This circuit has three sets of inputs.
1. Set of 16-bit inputs come from the outputs of AC.
2. Set of 16-bits come from the data register DR.
3. Set of 8-bit inputs come from the input register INPR.
 The result of an addition is transferred to AC and the end carry-out of the addition is transferred to flip-flop E (extended AC bit).
 The clock transition at the end of the cycle transfers the content of the bus into the designated destination register and the output of the adder and logic circuit into AC.

## Slide 19
Three control lines, S2, S1, and S0 control which register the bus selects as its input
0 0 0 x
0 0 1 AR
0 1 0 PC
0 1 1 DR
1 0 0 AC
1 0 1 IR
1 1 0 TR
1 1 1 Memory
S2 S1 S0 Register

## Slide 20: BASIC COMPUTER INSTRUCTIONS :
Basic Computer Instruction Format
15 14
12 11
0
I
Opcode
Address
Memory-Reference Instructions (OP-code = 000 ~ 110)
Register-Reference Instructions (OP-code = 111, I = 0)
Input-Output Instructions (OP-code =111, I = 1)
15
12 11
0
Register operation
0 1 1 1
15
12 11
0
I/O operation
1 1 1 1

## Slide 21: BASIC COMPUTER INSTRUCTIONS
Hex Code
Symbol I = 0 I = 1 Description
  AND 0xxx 8xxx AND memory word to AC
  ADD 1xxx 9xxx Add memory word to AC
  LDA 2xxx Axxx Load AC from memory
  STA 3xxx Bxxx Store content of AC into memory
  BUN 4xxx Cxxx Branch unconditionally
  BSA 5xxx Dxxx Branch and save return address
  ISZ 6xxx Exxx Increment and skip if zero
  CLA 7800 Clear AC
  CLE 7400 Clear E
  CMA 7200 Complement AC
  CME 7100 Complement E
  CIR 7080 Circulate right AC and E
  CIL 7040 Circulate left AC and E
  INC 7020 Increment AC
  SPA 7010 Skip next instr. if AC is positive
  SNA 7008 Skip next instr. if AC is negative
  SZA 7004 Skip next instr. if AC is zero
  SZE 7002 Skip next instr. if E is zero
  HLT 7001 Halt computer
  INP F800 Input character to AC
  OUT F400 Output character from AC
  SKI F200 Skip on input flag
  SKO F100 Skip on output flag
  ION F080 Interrupt on
  IOF F040 Interrupt off

## Slide 22: Basic working principle of the Control Unit with timing diagram :

## Slide 23
 Components of Control unit are
1. Two decoders
2. A sequence counter
3. Control logic gates
 An instruction read from memory is placed in the instruction register (IR). In control unit the IR is divided into three parts: I bit, the operation code (12-14)bit, and bits 0 through 11.
The operation code in bits 12 through 14 are decoded with a 3 X 8 decoder.
 Bit-15 of the instruction is transferred to a flip-flop designated by the symbol I.
 The eight outputs of the decoder are designated by the symbols D0 through D7. Bits 0 through 11 are applied to the control logic gates. The 4‐bit sequence counter can count in binary from 0 through 15.The outputs of counter are decoded into 16 timing signals T0 through T15.
 The sequence counter SC can be incremented or cleared synchronously. Most of the time, the counter is incremented to provide the sequence of timing signals out of 4 X 16 decoder. Once in awhile, the counter is cleared to 0, causing the next timing signal to be T0.
 As an example, consider the case where SC is incremented to provide timing signals T0, T1, T2, T3 and T4 in sequence. At time T4, SC is cleared to 0 if decoder output D3 is active. This is expressed symbolically by the statement
D3T4: SC ← 0

## Slide 24
Timing Diagram:
 The timing diagram figure shows the time relationship of the control signals.
 The sequence counter SC responds to the positive transition of the clock.
Initially, the CLR input of SC is active.
The first positive transition of the clock clears SC to 0, which in turn activates the timing T0 out of the decoder. T0 is active during one clock cycle.
The positive clock transition labeled T0 in the diagram will trigger only those registers whose control inputs are connected to timing signal T0.
SC is incremented with every positive clock transition, unless its CLR input is active.
This procedures the sequence of timing signals T0, T1, T2, T3 and T4, and so on. If SC is not cleared, the timing signals will continue with T5, T6, up to T15 and back to T0.
The last three waveforms shows how SC is cleared when D3T4 = 1. Output D3 from the operation decoder becomes active at the end of timing signal T2. When timing signal T4 becomes active, the output of the AND gate that implements the control function D3T4 becomes active.
 This signal is applied to the CLR input of SC. On the next positive clock transition the counter is cleared to 0. This causes the timing signal T0 to become active instead of T5 that would have been active if SC were incremented instead of cleared.

## Slide 26: Instruction Execution Cycle :
A program residing in the memory unit of the computer consists of a sequence of instructions. In the basic computer each instruction cycle consists of the following phases:
  Fetch an instruction from memory
  Decode the instruction
  Read the effective address from memory if the instruction has an indirect address
  Execute the instruction
After an instruction is executed, the cycle starts again at step 1, for the next instruction
This process continues unless a HALT instruction is encountered.
Note: Every different processor has its own (different) instruction cycle

## Slide 29
• Fetch and Decode
T0: AR PC (S0S1S2=010, T0=1)
T1: IR  M [AR], PC  PC + 1 (S0S1S2=111, T1=1)
T2: D0, . . . , D7  Decode IR(12-14), AR  IR(0-11), I  IR(15)
Initially, the program counter PC is loaded with the address of first instruction in the program.
The sequence counter SC is cleared to 0, providing a decoded timing signal T0.
After each clock pulse, SC is incremented by 1.
The following microoperation for fetch & decode phases can be specified by the following resister transfer statements.
Only AR is connected to address inputs of memory, AR PC with timing signal T0.
The instruction read from memory, IR  M [AR] with timing signal T1 & at the same time PC  PC + 1
At the time T2, the operation code in IR is decoded, the indirect bit I is transferred to flip-flop & address part of instruction is transferred to AR.
SC is incremented after each clock cycle pulse to produce the sequence T0, T1, T2.

## Slide 31
DETERMINE THE TYPE OF INSTRUCTION

## Slide 32
The flowchart presents an initial configuration for the instruction cycle and shows how the control determines the instruction type after the decoding.
Decoder output D7= 1, the instruction must be register-reference or input-output type.
If D7 = 0, the operation code must be one of the other seven values 110, specifying a memory reference instruction. (000 – 110)
Control then inspects the value of the first bit of the instruction, which now available in flip-flop I.
If D7 = 0 and I = 1, we have a memory-reference instruction with an indirect address. It is then necessary to read the effective address from memory.
 The three instruction types are subdivided into four separate paths. The selected operation is activated with the clock transition associated with timing signal T3.This can be symbolized as follows:
D’7 I T3 : AR  M[AR]
D’7 I ‘T3 : Nothing
D7 I ‘T3 : Execute a register-reference instr.
D7 I T3 : Execute an input-output instr.
D7 | I | 
0 | 1 | 
0 | 0 | 
1 | 0 | 
1 | 1 | 

## Slide 33
When a memory-reference instruction with I = 0 is encountered, it is not necessary to do anything since the effective address is already in AR.
However, the sequence counter SC must be incremented when D’7 I T3 = 1, so that the execution of the memory-reference instruction can be continued with timing variable T4.
 A register-reference or input-output instruction can be executed with the clock associated with timing signal T3. After the instruction is executed, SC is cleared to 0 and control returns to the fetch phase with T0 =1. SC is either incremented or cleared to 0 with every positive clock transition.

## Slide 34
REGISTER REFERENCE INSTRUCTIONS :
 When the register-reference instruction is decoded, D7 bit is set to 1.
 Each control function needs the Boolean relation D7 I' T3

## Slide 35: REGISTER REFERENCE INSTRUCTIONS :
r = D7 IT3 => Register Reference Instruction
Bi = IR(i) , i=0,1,2,...,11
- D7 = 1, I = 0
- Register Ref. Instr. is specified in b0 ~ b11 of IR
- Execution starts with timing signal T3
Register Reference Instructions are identified when
 These 12 bits are available in IR (0-11). They were also transferred to AR during time T2.
These instructions are executed at timing cycle T3.
 The first seven register-reference instructions perform clear, complement, circular shift, and increment microoperations on the AC or E registers.

## Slide 36
The next four instructions cause a skip of the next instruction in sequence when condition is satisfied. The skipping of the instruction is achieved by incrementing PC.
The condition control statements must be recognized as part of the control conditions. The AC is positive when the sign bit in AC(15) = 0; it is negative when AC(15) = 1.
The content of AC is zero (AC = 0) if all the flip-flops of the register are zero.
The HLT instruction clears a start-stop flip-flop S and stops the sequence counter from counting.
To restore the operation of the computer, the start-stop flip-flop must be set manually.

## Slide 37: Memory Reference Instructions :
 When the memory-reference instruction is decoded, D7 bit is set to 0.

## Slide 38
The effective address of the instruction is in the address register AR and was placed there during timing signal T2 when I = 0, or during timing signal T3 when I = 1.
 The execution of the memory-reference instructions starts with timing signal T4.
AND to AC
This is an instruction that performs the AND logic operation on pairs of bits in AC and the memory word specified by the effective address.
The result of the operation is transferred to AC.
D0T4: DRM[AR]
D0T5: AC  AC  DR, SC  0
ADD to AC
This instruction adds the content of the memory word specified by the effective address to the value of AC.
The sum is transferred into AC and the output carry Cout is transferred to the E (extended accumulator) flip-flop.
D1T4: DR  M[AR]
D1T5: AC  AC + DR, E  Cout, SC  0

## Slide 39
LDA: Load to AC
This instruction transfers the memory word specified by the effective address to AC.
D2T4: DR  M[AR]
D2T5: AC  DR, SC  0
STA: Store AC
This instruction stores the content of AC into the memory word specified by the effective address.
D3T4: M[AR]  AC, SC  0
BUN: Branch Unconditionally
This instruction transfers the program to instruction specified by the effective address.
The BUN instruction allows the programmer to specify an instruction out of sequence and the program branches (or jumps) unconditionally.
D4T4: PC  AR, SC  0

## Slide 40
BSA: Branch and Save Return Address
This instruction is useful for branching to a portion of the program called a subroutine or procedure.
When executed, the BSA instruction stores the address of the next instruction in sequence (which is available in PC) into a memory location specified by the effective address.
M[AR]  PC, PC  AR + 1
M[135] 21, PC 135 + 1 = 136

## Slide 41
It is not possible to perform the operation of the BSA instruction in one clock cycle when we use the bus system of the basic computer.
To use the memory and the bus properly, the BSA instruction must be executed with a sequence of two microoperations:
D5T4: M[AR]  PC, AR  AR + 1
D5T5: PC  AR, SC  0
ISZ: Increment and Skip if Zero
These instruction increments the word specified by the effective address, and if the incremented value is equal to 0, PC is incremented by 1.
Since it is not possible to increment a word inside the memory, it is necessary to read the word into DR, increment DR, and store the word back into memory.
D6T4: DR  M[AR]
D6T5: DR  DR + 1
D6T4: M[AR]  DR, if (DR = 0) then (PC  PC + 1), SC  0

## Slide 42: FLOWCHART FOR MEMORY REFERENCE INSTRUCTIONS :
Memory-reference instruction
DR  M[AR]
DR  M[AR]
DR  M[AR]
M[AR]  AC
SC  0
AND
ADD
LDA
STA
AC  AC DR
SC  0
AC  AC + DR
E  Cout
SC  0
AC  DR
SC  0
D T
0
4
D T
1
4
D T
2
4
D T
3
4
D T
0
5
D T
1
5
D T
2
5
PC  AR
SC  0
M[AR]  PC
AR  AR + 1
DR  M[AR]
BUN
BSA
ISZ
D T
4
4
D T
5
4
D T
6
4
DR  DR + 1
D T
5
5
D T
6
5
PC  AR
SC  0
M[AR]  DR
If (DR = 0)
then (PC  PC + 1)
SC  0
D T
6
6


## Slide 44: Input-Output Configuration of basic computer :
 A computer can serve no useful purpose unless it communicates with the external environment.
 To exhibit the most basic requirements for input and output communication, we will use a terminal unit with a keyboard and printer.
Input-output configuration
INPR Input register - 8 bits
OUTR Output register - 8 bits
FGI Input flag - 1 bit
FGO Output flag - 1 bit
IEN Interrupt enable - 1 bit

## Slide 45
The terminal sends and receives serial information
The serial info. from the keyboard is shifted into INPR
The serial info. for the printer is stored in the OUTR
INPR and OUTR communicate with the terminal serially and with the
AC in parallel.
The flags are needed to synchronize the timing difference between
I/O device and the computer.

## Slide 46
 The terminal sends and receives serial information and each quantity of information has eight bits of an alphanumeric code.
The serial information from the keyboard is shifted into the input register INPR.
 The serial information for the printer is stored in the output register OUTR.
These two registers communicate with a communication interface serially and with the AC in parallel.
 The transmitter interface receives serial information from the keyboard and transmits it to INPR. The receiver interface receives information from OUTR and sends it to the printer serially.
The 1-bit input flag FGI is a control flip-flop. It is set to 1 when new information is available in the input device and is cleared to 0 when the information is accepted by the computer.
The flag is needed to synchronize the timing rate difference between the input device and the computer.
 The process of information transfer is as follows:

## Slide 47
The process of input information transfer:
 Initially, the input flag FGI is cleared to 0. When a key is struck in the keyboard, an 8-bit alphanumeric code is shifted into INPR and the input flag FGI is set to 1.
 As long as the flag is set, the information in INPR cannot be changed by striking another key. The computer checks the flag bit; if it is 1, the information from INPR is transferred in parallel into AC and FGI is cleared to 0.
Once the flag is cleared, new information can be shifted into INPR by striking another key.
The process of outputting information:
 The output register OUTR works similarly but the direction of information flow is reversed.
 Initially, the output flag FGO is set to 1. The computer checks the flag bit; if it is 1, the information from AC is transferred in parallel to OUTR and FGO is cleared to 0. The output device accepts the coded information, prints the corresponding character, and when the operation is completed, it sets FGO to 1.
 The computer does not load a new character into OUTR when FGO is 0 because this condition indicates that the output device is in the process of printing the character.

## Slide 48: Input-Output instructions :
 Input and output instructions are needed for transferring information to and from AC register, for checking the flag bits, and for controlling the interrupt facility.
 Input-output instructions have an operation code 1111 and are recognized by the control when D7 = 1 and I = 1.
 The remaining bits of the instruction specify the particular operation.
 The control functions and microoperations for the input-output instructions are listed below.

## Slide 49: Input-Output instructions :
D7IT3 = p
IR(i) = Bi, i = 6, …, 11
p: SC  0 Clear SC
INP pB11: AC(0-7)  INPR, FGI  0 Input char. to AC
OUT pB10: OUTR  AC(0-7), FGO  0 Output char. from AC
SKI pB9: if(FGI = 1) then (PC  PC + 1) Skip on input flag
SKO pB8: if(FGO = 1) then (PC  PC + 1) Skip on output flag
ION pB7: IEN  1 Interrupt enable on
IOF pB6: IEN  0 Interrupt enable off
Input and output instructions are needed for transferring information to and from AC register, for checking the flag bits, and for controlling the interrupt facility.
Input-output instructions have an operation code 1111 and are recognized by the control when D7 = 1 and I = 1.
The remaining bits of the instruction specify the particular operation.
 The control functions and microoperations for the input-output instructions are listed below.

## Slide 50
The INP instruction transfers the input information from INPR into the eight low-order bits of AC and also clears the input flag to 0.
The OUT instruction transfers the eight least significant bits of AC into the output register OUTR and clears the output flag to 0.
The next two instructions in Table 2.2 check the status of the flags and cause a skip of the next instruction if the flag is 1.
The instruction that is skipped will normally be a branch instruction to return and check the flag again.
The branch instruction is not skipped if the flag is 0. If the flag is 1, the branch instruction is skipped and an input or output instruction is executed.
 The last two instructions set and clear an interrupt enable flip-flop IEN. The purpose of IEN is explained in conjunction with the interrupt operation.

## Slide 51: Interrupt Cycle :

## Slide 52
 An interrupt flip-flop R is included in the computer.
 When R = 0, the computer goes through an instruction cycle.
 During the execute phase of the instruction cycle IEN is checked by the control.
 If it is 0, it indicates that the programmer does not want to use the interrupt, so control continues with the next instruction cycle.
 If IEN is 1, control checks the flag bits.
 If both flags are 0, it indicates that neither the input nor the output registers are ready for transfer of information.
 In this case, control continues with the next instruction cycle. If either flag is set to 1 while IEN = 1, flip-flop R is set to 1.
At the end of the execute phase, control checks the value of R, and if it is equal to 1, it goes to an interrupt cycle instead of an instruction cycle.
Interrupt Cycle
 The interrupt cycle is a hardware implementation of a branch and save return address operation.
 The return address available in PC is stored in a specific location where it can be found later when the program returns to the instruction at which it was interrupted. This location may be a processor register, a memory stack, or a specific memory location.

## Slide 53
 Here we choose the memory location at address 0 as the place for storing the return address.
 Control then inserts address 1 into PC and clears IEN and R so that no more interruptions can occur until the interrupt request from the flag has been serviced.
 An example that shows what happens during the interrupt cycle is shown in Figure
 Suppose that an interrupt occurs and R = 1, while the control is executing the instruction at address 255. At this time, the return address 256 is in PC.

## Slide 54
 The programmer has previously placed an input-output service program in memory starting from address 1120 and a BUN 1120 instruction at address 1.
The content of PC (256) is stored in memory location 0, PC is set to 1, and R is cleared to 0.
At the beginning of the next instruction cycle, the instruction that is read from memory is in address 1 since this is the content of PC. The branch instruction at address 1 causes the program to transfer to the input-output service program at address 1120.
This program checks the flags, determines which flag is set, and then transfers the required input or output information. Once this is done, the instruction ION is executed to set IEN to 1 (to enable further interrupts), and the program returns to the location where it was interrupted.
The instruction that returns the computer to the original place in the main program is a branch indirect instruction with an address part of 0. This instruction is placed at the end of the I/O service program.
 The execution of the indirect BUN instruction results in placing into PC the return address from location 0.

## Slide 55: Complete Computer Description: Flowchart for basic computer

## Slide 56: Design of Basic Computer :

## Slide 59: Design of Accumulator Unit:
 The circuits associated with the AC register are shown in figure 2.16.

## Slide 60
 The adder and logic circuit has three sets of inputs.
 One set of 16 inputs comes from the outputs of AC.
 Another set of 16 inputs comes from the data register DR.
 A third set of eight inputs comes from the input register INPR.
 The outputs of the adder and logic circuit provide the data inputs for the register.
 In addition, it is necessary to include logic gates for controlling the LD, INR, and CLR in the register and for controlling the operation of the adder and logic circuit.
In order to design the logic associated with AC, it is necessary to extract all the statements that change the content of AC.
            D0T5: AC ← AC ∧ DR AND with DR
            D1T5: AC ← AC + DR Add with DR
            D2T5: AC ← DR Transfer from DR
            pB11: AC(0-7) ← INPR Transfer from INPR
            rB9: AC ← AC’ Complement
            rB7: AC ← shr AC, AC(15) ← E Shift right
            rB6: AC ← shl AC, AC(0) ← E Shift left
            rB11: AC ← 0 Clear
            rB5: AC ← AC + 1 Increment

## Slide 61
 The gate structure that controls the LD, INR, and CLR inputs of AC is shown in figure

## Slide 62
The gate configuration is derived from the control functions in the list above.
The control function for the clear microoperation is rB11, where r = D7I’T3 and B11 = IR (11).
The output of the AND gate that generates this control function is connected to the CLR input of the register.
Similarly, the output of the gate that implements the increment microoperation is connected to the INR input of the register.
The other seven microoperations are generated in the adder and logic circuit and are loaded into AC at the proper time.
 The outputs of the gates for each control function are marked with a symbolic name and used in the design of the adder and logic circuit.