## Slide 1: Unit – 4 Central Processing Unit

## Slide 2: Topics to be covered
Introduction
General Register Organization
Stack Organization
Instruction format
Addressing Modes
Data transfer and manipulation
Program Control
Reduced Instruction Set Computer (RISC)
Complex Instruction Set Computer (CISC)

## Slide 3: General Register Organization

## Slide 4
R1
R2
R3
R4
R5
R6
R7
MUX - A
MUX - B
Arithmetic Logic Unit
(ALU)
3x8
decoder
Clock
Input
Output
SEL B
SEL A
SEL D
OPR
Load
(7 lines)
A - bus
B - bus

## Slide 5: General Register Organization
Example: R1 R2 + R3
To perform the above operation, the control must provide binary selection variables to the following selector inputs:
MUX A selector (SELA): to place the content of R2 into bus A.
MUX B selector (SELB): to place the content of R3 into bus B.
ALU operation selector (OPR): to provide the arithmetic addition A + B.
Decoder destination selector (SELD): to transfer the content of the output bus into R1.
Control Word:
SELA
SELB
SELD
OPR

## Slide 6: General Register Organization
Binary Code | SELA | SELB | SELD
000 | Input | Input | None
001 | R1 | R1 | R1
010 | R2 | R2 | R2
011 | R3 | R3 | R3
100 | R4 | R4 | R4
101 | R5 | R5 | R5
110 | R6 | R6 | R6
111 | R7 | R7 | R7
OPR Select | Operation | Symbol
00000 | Transfer A | TSFA
00001 | Increment A | INCA
00010 | A + B | ADD
00101 | A – B | SUB
00110 | Decrement A | DECA
01000 | A and B | AND
01010 | A or B | OR
01100 | A xor B | XOR
01110 | Complement A | COMA
10000 | Shift right A | SHRA
11000 | Shift left A | SHLA
Encoding of Register Selection Fields
Encoding of ALU Operations

## Slide 7: Stack Organization

## Slide 8: Stack Organization
A stack is a storage device that stores information in such a manner that the item stored last is the first item retrieved (LIFO).
The register that holds the address for the stack is called a stack pointer (SP) because its value always points at the top item in the stack.
The physical registers of a stack are always available for reading or writing. It is the content of the word that is inserted or deleted.
There are two types of stack organization
  Register stack – built using registers
  Memory stack – logical part of memory allocated as stack

## Slide 9: Register Stack
C
B
A
DR
FULL
EMTY
SP
63
3
2
1
0
4
Address

## Slide 10: Register Stack
A stack can be placed in a portion of a large memory or it can be organized as a collection of a finite number of memory words or registers. Figure shows the organization of a 64-word register stack.
The stack pointer register SP contains a binary number whose value is equal to the address of the word that is currently on top of the stack.
In a 64-word stack, the stack pointer contains 6 bits because 26 = 64.
Since SP has only six bits, it cannot exceed a number greater than 63 (111111 in binary).
The one-bit register FULL is set to 1 when the stack is full, and the one-bit register EMTY is set to 1 when the stack is empty of items.
DR is the data register that holds the binary data to be written into or read out of the stack.

## Slide 11: Register Stack
PUSH Operation
SP ← SP + 1
M[SP] ← DR
IF (SP= 0) then (FULL ← 1)
EMTY ← 0
POP Operation
DR ← M[SP]
SP ← SP - 1
IF (SP= 0) then (EMTY ← 1)
FULL ← 0

## Slide 12: Memory Stack
Program
(instructions)
Data
(operands)
Stack
DR
1000
Address
2000
3000
3997
3998
3999
4000
4001
PC
AR
SP

## Slide 13: Memory Stack
The implementation of a stack in the CPU is done by assigning a portion of memory to a stack operation and using a processor register as a stack pointer.
Figure shows a portion of computer memory partitioned into three segments: program, data, and stack.
The program counter PC points at the address of the next instruction in the program which is used during the fetch phase to read an instruction.
The address registers AR points at an array of data which is used during the execute phase to read an operand.
The stack pointer SP points at the top of the stack which is used to push or pop items into or from the stack.
We assume that the items in the stack communicate with a data register DR.

## Slide 14: Memory Stack
PUSH Operation
SP ← SP - 1
M[SP] ← DR
POP Operation
DR ← M[SP]
SP ← SP + 1

## Slide 15: Reverse Polish Notation
The common mathematical method of writing arithmetic expressions imposes difficulties when evaluated by a computer.
The Polish mathematician Lukasiewicz showed that arithmetic expressions can be represented in prefix notation as well as postfix notation.
A + B
+ AB
AB +
Infix
Prefix or Polish
Postfix or reverse Polish
A * B + C * D
AB * CD * +
Reverse Polish

## Slide 16: Evaluation of Arithmetic Expression
(3 * 4) + (5 * 6)
3 4 * 5 6 * +
3
4
3
12
5
12
6
5
12
30
12
42
3
4
*
5
6
*
+
42

## Slide 17: Instruction Formats

## Slide 18: Instruction Formats
Instructions are categorized into different formats with respect to the operand fields in the instructions.
  Three Address Instructions
  Two Address Instruction
  One Address Instruction
  Zero Address Instruction
  RISC Instructions

## Slide 19: Three Address Instruction
Computers with three-address instruction formats can use each address field to specify either a processor register or a memory operand.
The program in assembly language that evaluates X = (A + B) * (C + D) is shown below.
The advantage of three-address format is that it results in short programs when evaluating arithmetic expressions.
The disadvantage is that the binary-coded instructions require too many bits to specify three addresses.
ADD R1, A, B
R1← M[A]+ M[B]
ADD R2, C, D
R2← M[C]+ M[D]
MUL X, R1, R2
M[X]← R1 * R2

## Slide 20: Two Address Instruction
Two address instructions are the most common in commercial computers. Here again each address field can specify either a processor register or a memory word.
The program to evaluate X = (A + B) * (C + D) is as follows:
MOV R1, A
R1← M[A]
ADD R1, B
R1← R1+ M[B]
MOV R2, C
R2← M[C]
ADD R2, D
R2← R2+ M[D]
MUL R1, R2
R1← R1 * R2
M[X]← R1
MOV X, R1

## Slide 21: One Address Instruction
One address instructions use an implied accumulator (AC) register for all data manipulation.
For multiplication and division these is a need for a second register.
However, here we will neglect the second register and assume that the AC contains the result of all operations.
The program to evaluate X = (A + B) * (C + D) is
LOAD A
AC← M[A]
ADD B
AC← AC+M[B]
STORE T
M[T]←AC
LOAD C
AC← M[C]
ADD D
AC← AC+M[D]
MUL T
AC← AC*M[T]
STORE X
M[X]←AC

## Slide 22: Zero Address Instruction
A stack-organized computer does not use an address field for the instructions ADD and MUL.
The PUSH and POP instructions, however, need an address field to specify the operand that communicates with the stack.
The program to evaluate X = (A + B) * (C + D) will be written for a stack-organized computer.
To evaluate arithmetic expressions in a stack computer, it is necessary to convert the expression into reverse polish notation.
PUSH A
TOS← M[A]
PUSH B
TOS← M[B]
ADD
TOS←(A+B)
PUSH C
TOS← M[C]
PUSH D
TOS← M[D]
ADD
TOS←(C+D)
MUL
TOS←(C+D)*(A+B)
POP X
M[X] ← TOS

## Slide 23: RISC Instruction
The instruction set of a typical RISC processor is restricted to the use of load and store instructions when communicating between memory and CPU.
All other instructions are executed within the registers of the CPU without referring to memory.
A program for a RISC type CPU consists of LOAD and STORE instructions that have one memory and one register address, and computational-type instructions that have three addresses with all three specifying processor registers.
The following is a program to evaluate X = (A + B) * (C + D)
LOAD R1, A
R1← M[A]
LOAD R2, B
R2← M[B]
LOAD R3, C
R3← M[C]
LOAD R4, D
R4← M[D]
ADD R1, R1, R2
R1← R1+R2
ADD R3, R3, R4
R3← R3+R4
MUL R1, R1, R3
R1← R1*R3
STORE X, R1
M[X] ← R1

## Slide 24: Addressing Modes

## Slide 25: Addressing Modes
The addressing mode specifies a rule for interpreting or modifying the address field of the instruction before the operand is actually referenced.
Computers use addressing mode techniques for the purpose of accommodating one or both of the following provisions:
  To give programming versatility to the user by providing such facilities as pointers to memory, counters for loop control, indexing of data, and program relocation.
  To reduce the number of bits in the addressing field of the instruction.
There are basic 10 addressing modes supported by the computer.

## Slide 26
Addressing Mode :
Implied Mode (Implicit Mode)
Immediate Mode
Register mode
Register indirect mode
Autoincrement or Autodecrement mode
Direct address mode
Indirect address mode
Relative address mode
Indexed address mode
Base Register address mode

## Slide 27: 1. Implied Mode (Implicit Mode) :
Operand is specified implicitly in the definition of instruction.
Used for zero address and one address instructions.
INCA – Increment AC : AC  AC + 1
CMA – Complement Accumulator
ADD – Addition of two value from Stack
Opcode | Address

## Slide 28: 2. Immediate Mode:
Operand is specified in the instruction itself.
Instructions has an operand field rather than an address field.
Useful for initializing registers to a constant value.
Opcode | Mode | Address (Operand)
immediate
Operand value

## Slide 29: 3. Register Mode: (Absolute Mode)
Address part of instruction specifies a register, which holds the operand.
Operand is present in the register.
Register number is written in instruction.
Address field of instruction specifies effective address.
ADD R1 R2
R1  R1 + R2
Register No
Opcode | Mode | Address (Operand)

## Slide 30: 4. Register Indirect Mode :
Register contains address of operand rather than operands itself.
Used to shorten the instruction length.
ADD R1,(R2) : R1  R1 + M[(R2)]

## Slide 31
Assume a system with 4GB main memory & CPU has 64 general purpose registers.
MM add = 32 bit
Register references = 6 bit

## Slide 32: 5. Autoincrement or Autodecrement Mode :
Used to access table of content (array) sequentially.
Variant of register indirect mode.
Content of register (effective address) is Automatically increment or decrement.

## Slide 33: 6. Direct Addressing Mode : (Absolute Addressing Mode)
Actual address is given in the instruction.
Use to access variable.

## Slide 34: 7. Indirect Addressing Mode :
Used to implement pointer and passing parameters.
2 memory access required.
ADD X
AC  AC + M [ M[X] ]
EA = 800
EA = M [x]

## Slide 35: 8. Relative Addressing Mode :
Used for program control instruction like branch & jump.
Effective Address = Program counter + Address part of instruction
EA = PC + Offset (Displacement)
EA = 501 + 50 = 551 - False
EA = 501 + 49 = 550 - True

## Slide 36: 9. Base Register Addressing Mode :
Used in program relocation.
Main memory size limited – So process swap in & swap out frequently
Change the location of process in main memory
BR 160
BR 160
BR 60
EA = Base Register value + Displacement
= 400 +60 = 460
Base Register store the base address value.

## Slide 37: 10. Indexed Addressing Mode :
Use to access or implement array efficiently
Multiple register required to implement
Any element can be accessed without change in instruction
100
101
102
103
104
EA = Base + Indexed Register value
= 100 +4 = 104
Opcode | Address
BA = 100

## Slide 38
Opcode | Mode | Address (Operand)
500
Index Register
201
500
500
800
800
300
400
---
400
700
399
450
500+100 = 600
900
202+500 = 702
---
Target Inst.

## Slide 39: Data transfer & manipulation instructions

## Slide 40: Data transfer instructions
Data transfer instructions move data from one place in the computer to another without changing the data content.
The most common transfers are between memory and processor registers, between processor registers and input or output, and between the processor registers themselves.
Name | Mnemonic
Load | LD
Store | ST
Move | MOV
Exchange | XCH
Input | IN
Output | OUT
Push | PUSH
Pop | POP

## Slide 41: Data manipulation instructions
Data manipulation instructions perform operations on data and provide the computational capabilities for the computer.
The data manipulation instructions in a typical computer are usually divided into three basic types:
  Arithmetic instructions
  Logical and bit manipulation instructions
  Shift instructions

## Slide 42: 1. Arithmetic Instructions
Name | Mnemonic
Increment | INC
Decrement | DEC
Add | ADD
Subtract | SUB
Multiply | MUL
Divide | DIV
Add with carry | ADDC
Subtract with borrow | SUBB
Negate (2’s complement) | NEG

## Slide 43: 2. Logical & Bit Manipulation Instructions
Name | Mnemonic
Clear | CLR
Complement | COM
AND | AND
OR | OR
Exclusive-OR | XOR
Clear carry | CLRC
Set carry | SETC
Complement carry | COMC
Enable interrupt | EI
Disable interrupt | DI

## Slide 44: 3. Shift Instructions
Name | Mnemonic
Logical shift right | SHR
Logical shift left | SHL
Arithmetic shift right | SHRA
Arithmetic shift left | SHLA
Rotate right | ROR
Rotate left | ROL
Rotate right through carry | RORC
Rotate left through carry | ROLC

## Slide 45: Program Control

## Slide 46: Program Control
A program control type of instruction, when executed, may change the address value in the program counter and cause the flow of control to be altered.
The change in value of the program counter as a result of the execution of a program control instruction causes a break in the sequence of instruction execution.
Name | Mnemonic
Branch | BUN
Jump | JMP
Skip | SKP
Call | CALL
Return | RET
Compare (by subtraction) | CMP
Test (by ANDing) | TST

## Slide 47: Status Bit Conditions
8-bit ALU
A
B
8
8
V | Z | S | C
Check for zero output
8
Output F

## Slide 48: Status Bit Conditions
Bit C (carry) is set to 1 if the end carry C8 is 1. It is cleared to 0 if the carry is 0.
Bit S (sign) is set to 1 if the highest-order bit F7 is 1. It is set to 0 if the bit is 0.
Bit Z (zero) is set to 1 if the output is zero and Z = 0 if the output is not zero.
Bit V (overflow) is set to 1 if the exclusive-OR of the last two carries is equal to 1, and cleared to 0 otherwise. This is the condition for an overflow when negative numbers are in 2’s complement.

## Slide 49: Conditional Branch Instructions
Mnemonic | Branch Condition | Tested Condition
BZ | Branch if zero | Z = 1
BNZ | Branch if not zero | Z = 0
BC | Branch if carry | C = 1
BNC | Branch if no carry | C = 0
BP | Branch if plus | S = 0
BM | Branch if minus | S = 1
BV | Branch if overflow | V = 1
BNV | Branch if no overflow | V = 0
Unsigned compare conditions (A – B) |  | 
BHI | Branch if higher | A > B
BHE | Branch if higher or equal | A ≥ B
BLO | Branch if lower | A < B

## Slide 50: Conditional Branch Instructions
Mnemonic | Branch Condition | Tested Condition
BLOE | Branch if lower or equal | A ≤ B
BE | Branch if equal | A = B
BNE | Branch if not equal | A ≠ B
Signed compare conditions (A – B) |  | 
BGT | Branch if greater than | A > B
BGE | Branch if greater or equal | A ≥ B
BLT | Branch if less than | A < B
BLE | Branch if less or equal | A ≤ B
BE | Branch if equal | A = B
BNE | Branch if not equal | A ≠ B

## Slide 51: Program Interrupt
The interrupt procedure is, in principle, quite similar to a subroutine call except for three variations:
  The interrupt is usually initiated by an internal or external signal rather than from the execution of an instruction.
  The address of the interrupt service program is determined by the hardware rather than from the address field of an instruction.
  An interrupt procedure usually stores all the information necessary to define the state of the CPU rather than storing only the program counter.
After a program has been interrupted and the service routine been executed, the CPU must return to exactly the same state that it was when the interrupt occurred. Only if this happens will the interrupted program be able to resume exactly as if nothing had happened.

## Slide 52: Program Interrupt
The state of the CPU at the end of the execute cycle (when the interrupt is recognized) is determined from:
  The content of the program counter
  The content of all processor registers
  The content of certain status conditions
The interrupt facility allows the running program to proceed until the input or output device sets its ready flag. Whenever a flag is set to 1, the computer completes the execution of the instruction in progress and then acknowledges the interrupt.
 The result of this action is that the return address is started in location 0. The instruction in location 1 is then performed; this initiates a service routine for the input or output transfer. The service routine can be stored in location 1.

## Slide 54
The service routine must have instructions to perform the following tasks:
1. Save contents of processor registers.
2. Check which flag is set.
3. Service the device whose flag is set.
4. Restore contents of processor registers.
5. Turn the interrupt facility on.
6. Return to the running program.

## Slide 55: Program Status Word (PSW)
The collection of all status bit conditions in the CPU is sometimes called a program status word or PSW.
The PSW is stored in a separate hardware register and contains the status information that characterizes the state of the CPU.

## Slide 56: Types of interrupts
There are three major types of interrupts that cause a break in the normal execution of a program. They can be classified as:
  External interrupts
  Internal interrupts
  Software interrupts

## Slide 57: 1. External Interrupt
External interrupts come from
  Input-output (I/O) devices
  Timing device
  Circuit monitoring the power supply
  Any other external source
Examples that cause external interrupts are
  I/O device requesting transfer of data
  I/O device finished transfer of data
  Elapsed time of an event
  Power failure
External interrupts are asynchronous.
External interrupts depend on external conditions that are independent of the program being executed at the time.

## Slide 58: 2. Internal interrupts (Traps)
Internal interrupts arise from Illegal or erroneous use of an instruction or data. Internal interrupts are also called traps.
Examples of interrupts caused by internal error conditions like
  Register overflow
  Attempt to divide by zero
  invalid operation code
  stack overflow
  protection violation.
These error conditions usually occur as a result of a premature termination of the instruction execution.
Internal interrupts are synchronous with the program. If the program is rerun, the internal interrupts will occur in the same place each time.

## Slide 59: 3. Software interrupts
A software interrupt is a special call instruction that behaves like an interrupt rather than a subroutine call.
The most common use of software interrupt is associated with a supervisor call instruction. This instruction provides means for switching from a CPU user mode to the supervisor mode.
When an input or output transfer is required, the supervisor mode is requested by means of a supervisor call instruction. This instruction causes a software interrupt that stores the old CPU state and brings in a new PSW that belongs to the supervisor mode.
The calling program must pass information to the operating system in order to specify the particular task requested.

## Slide 60: Reduced Instruction Set Computer (RISC)

## Slide 61: Reduced Instruction Set Computer (RISC)
Characteristics of RISC are as follows:
  Relatively few instructions
  Relatively few addressing modes
  Memory access limited to load and store instructions
  All operations done within the registers of the CPU
  Fixed-length, easily decoded instruction format
  Single-cycle instruction execution
  Hardwired rather than microprogrammed control
  A relatively large number of registers in the processor unit
  Use of overlapped register windows to speed-up procedure call and return
  Efficient instruction pipeline
  Compiler support for efficient translation of high-level language programs into machine language programs

## Slide 62: Complex Instruction Set Computer (CISC)

## Slide 63: Complex Instruction Set Computer (CISC)
Characteristics of CISC are as follows:
  A larger number of instructions – typically from 100 to 250 instructions
  Some instructions that perform specialized tasks and are used infrequently
  A large variety of addressing modes – typically from 5 to 20 different modes
  Variable-length instruction formats
  Instructions that manipulate operands in memory

## Slide 64: Overlapped Register Window
A characteristic of some RISC processors is their use of overlapped register windows to provide the passing of parameters and avoid the need for saving and restoring register values.
Each procedure call results in the allocation of a new window consisting of a set of registers from the register file for use by the new procedure.
Windows for adjacent procedures have overlapping registers that are shared to provide the passing of parameters and results.

## Slide 65: Overlapped Register Window
R15
R10
R73
R64
R63
R58
R57
R48
R47
R42
R41
R32
R31
R26
R25
R16
R15
R10
R9
R0
Global registers
Common to all procedures
Common to D and A
Local to D
Common to C and D
Common to B and C
Common to A and B
Common to A and D
Local to C
Local to B
Local to A
Proc A
Proc D
Proc C
Proc B
Window size = L + 2C + G
Register file = (L + C) W + G

## Slide 66: Overlapped Register Window
Suppose that procedure A calls procedure B.
Registers R26 through R31 are common to both procedures, and therefore procedure A stores the parameters for procedure B in these registers.
Procedure B uses local registers R32 through R41 for local variable storage.
If procedure B calls procedure C, it will pass the parameters through registers R42 through R47.
When procedure B is ready to return at the end of its computation, the program stores results of the computation in registers R26 through R31 and transfers back to the register window of procedure A.
Note that registers R10 through R15 are common to procedures A and D because the four windows have a circular organization with A being adjacent to D.

## Slide 67
The concept of overlapped register windows is shown in figure. The system had a total of 74 registers. Register R0 through R9 are global registers that hold parameters shared by all procedures.
The other 64 registers are divided into four windows to accommodate procedure A, B, C and D. Each register window consists of 10 local registers and two sets of six registers common to adjacent windows.
Only one register window is activated at any given time with a pointer indicating the active window.
The high register of the calling procedure overlap the low registers of the called procedure, and therefore the parameters automatically transfer from calling to called procedure.

## Slide 68
The organization of register windows will have the following relationships:
Number of global registers = G
Number of local registers in each window = L
Number of register common to two windows = C
Number of windows = W
The number of registers available for each window is calculated as follows:
Window size = L + 2C + G = 10 + 2*6 + 10 = 32
The total number of register needed in the processor is
Register file = (L + C) W + G = (10 + 6 ) *4 + 10 = 74

## Slide 69
RISC | CISC
Reduced instruction set computer | Complex instruction set computer
There are few addressing modes. Most instructions have register to register addressing modes. | There are many addressing modes.
There are few instructions. | There are many instructions.
It can include simple instructions and takes one cycle. | It can include complex instructions and takes multiple cycles.
Hardware executes the instructions. | Micro-program executes the instructions.
There are Fixed format instructions. | There are Variable format instructions.
It can be easier to decode as instructions have a fixed format. | It can be complex to decode as instructions have variable format.
There are multiple register sets are used. | A single register set is used.
RISC is highly pipelined. | CISC is not pipelined or less pipelined.
Require more RAM. | Require less RAM